## Slide 1: Design Technology Co-Optimization for In-Memory Search
Speaker : B11901027 王仁軒
Mentor : Rick Huang
Date : 2025/05/02

## Slide 2: Outline
Introduction to few-shot learning
von Neumann architecture vs in-memory architecture
Choices of memory
  Volatile vs Non-volatile
Searching methods
  Exact-Match vs Best-Match
Distance metrics and its realization
  Norm
  Norm
Difficulties of Best-Match searching method
  Sources of analog non-idealities
  Methods in CIM to overcome analog noises

## Slide 3: Few Shot Learning
Traditional classification models suffers from catastrophic forgetting when learning new domains
Tackle the forgetting issue
  Search ALL data stored in the memory
Classfier
Forgets about cats
  Cosine similarity!
Cosine similarity

## Slide 4: Von Neumann Architecture
Traditional computer requires frequent data transfer between CPU and RAM for ML tasks
In memory search structure
  60%↑power
  von Neumann bottleneck
  Parallel !
  Scalable !
  0
  0
  0
  1
Need extra ckt to perform “Search” and represent “don’t cares”

## Slide 5: Types of Memory (TCAM)
TCAM : Ternary content addressable memory
Volatile vs Non-Volatile
16T CMOS
Cannot cut off power
More transistors
LEAKAGE!!!
2T Flash/FeFET
Low power
Compact design
Low leakage
2T RRAM Crossbar
Low power
Compact design
Acceptable leakage
SRAM

## Slide 6: Types of Searching
Exact-match vs Best-match TCAM
0
1
0
1
HIT !
HIT !
Difference
Don’t require complex circuit | Require analog circuit (ADC…)
Can scale up to MB/GB | Scale is limited to kB due to analog non-idealities and area
Functionality is restricted (need Special Encoding) | Finds the most similar entry (bitwise hamming distance)
1
0
2
0
Used in large scale tasks
Used in small scale tasks

## Slide 7: From Angular to Distance Metric
Cosine similarity
Compute floating-point value is costly
Quantize the model to int
Computation cost
Use other metric rather than cos_sim
Hamming Distance ?
norm : d1 + d2 ?
norm : Max( d1 , d2 ) ?
Norm : d
d1
d2
Int8 for each dimension

## Slide 8: Exact-Match Search with Norm
norm – Using exact-match search
  Find the smallest square containing the query
  Encode ranges into ternary vector
    Represent a square using ranges
    If query is in the range: HIT !
More space Short time
Iterative !
Less space Long time
query
query
Iteratively expand from query
Class green
Create squares from existing data
1
2
3
1
Ref: Encoding Short Ranges in TCAM Without Expansion: Efficient Algorithm and Applications

## Slide 9: Range Encoding
norm
  Realization of “Squares”
  Gray code varies 1b for neighbors
    Good for encoding ranges
    But has some restrictions
      Range Starts from
      length =
00
01
11
10
0*
1*
*1
*0
*0
Gray code
0
1
2
3
4-bit example
Gray code + offset ( postfix ) + Intersection
Offset
0
1
2
3
4
[3,5] = [2,5] [3:6]
5
Ref: Encoding Short Ranges in TCAM Without Expansion: Efficient Algorithm and Applications
Range = 2 OK
Range = 3 Fail
**

## Slide 10: Best-Match Search with Norm
norm ( Hamming distance) – Using best-match search
  Regular method : Use 8-bit ADC
  Method to avoid using ADC : cut the data into segments
V
Low Vt Sence Amp
High Vt Sence Amp
B
A
AB = 00 / 10 / 11
Diff = 2 1 0
Can binary bits represent decimal norm well?
1 0 1 1 0 0 1 1
1 1 0 0 0 0 1 1
1
2
0
0
+
3
15-11=4 but 1111–1011 = 1
Thermometer code
0 -> 00000000
3 -> 00000111
5 -> 00011111
Avoids using 2-bit ADC
Ref: SAPIENS: A 64-Kbit RRAM-Based Non-Volatile Associative Memory for One-Shot Learning and Inference at the Edge

## Slide 11: Problems of Best-Match TCAM
Analog non-idealities
  Noise of storage elements accumulates
  Parasitic effects of Match-Line
noise
noise
noise
noise
Large variation
Ref: Experimentally validated memristive memory augmented neural network with efficient hashing and similarity search

## Slide 12: Problems of Best-Match TCAM
Analog non-idealities
  Noise of storage elements accumulates
  Parasitic effects of Match-Line
Position affects discharge rate
Mismatch here are less sensitive
( large denominator )
Mismatch here are more sensitive
( small denominator)
Match : small G
Mismatch : large G
RAM array
Eq. ckt model
To ADC
ML
To ADC
Ref: In-Memory Nearest Neighbor Search With Nanoelectromechanical Ternary Content-Addressable Memory

## Slide 13: Overcome Analog Non-Ideal Effects
Analog non-idealities
  Noise-aware training (Compute-in-memory case)
    Noise of analog circuits could hazard our performance
    Inject noise into model to make it noise-resistant
or more complicated
device noise model (costly)
w/o noise injection
w/ noise
injection
What if we inject noise into embeddings?
Ref: In-Memory Computing Advances and Prospects

## Slide 14: Conclusions and Future Work
Choices of memory
  Non-volatile memory can be compact and energy-efficient
Searching methods
  Use exact-match for big tasks and best-match for small tasks
Distance metrics
  Use and Norm to replace cosine similarity
Challenges of best-match search
  Analog noise and parasitic effects are challenging
Future Work
  Apply the method used in CIM to Overcome Analog non-ideal effects
  Does and Norm performs as good as cosine similarity