## Slide 1: Design Technology Co-Optimization for In-Memory Search
Speaker: B11901027 王仁軒

## Slide 2: Outline
Introduction to few-shot learning
Traditional computer architecture vs In-memory searching
Choices of memory
  Volatile vs Non-volatile
Searching methods
  Exact-Match vs Best-Match
Distance metrics and its realization
  L-infinity norm
  L-1 norm
Difficulties of Best-Match searching method
  Sources of analog non-idealities
  Methods in CIM to tackle analog noises

## Slide 3: Few/One Shot Learning
Traditional classification models suffers from catastrophic forgetting when learning new domains
Tackle the forgetting issue
  Search ALL data stored in the memory
Classfier
Forgets about cats
  Cosine similarity!

## Slide 4: Traditional computer architecture
Traditional computer requires frequent data transfer between CPU and RAM for ML tasks
In memory search structure
  60%↑power
  von Neumann bottleneck
  Parallel !
  Scalable !
  0
  0
  0
  1
The array structure of memory allows us to lower the complexity of computing

## Slide 5: Types of Memory
Volatile vs Non-Volatile
16T CMOS
Cannot cut off power
LEAKAGE!!!
2T Flash/FeFET
Low power
Low leakage
2T RRAM Crossbar
Low power
Acceptable leakage

## Slide 6: Types of Searching
Exact-match vs Best-match TCAM
0
1
0
1
1
0
2
0
HIT !
HIT !
Difference
Don’t require complex circuit for post processing | Require other analog circuit (Winner Take All ckt, ADC…)
Can scale up to MB/GB | Scale is limited to kB due to analog non-idealities and area
Functionality is restricted (need Special Encoding) | Finds the most similar entry (hamming distance)

## Slide 7: Distance metric
Cosine similarity
Not friendly for direct hardware implementation
Binary data possess spatial info
Not angular info
Spatial metric may be binary-friendly
Hamming Distance ?
d1 + d2 ?
Max( d1 , d2 ) ?
d
d1
d2

## Slide 8: Distance metric
L-infinity norm
  Find the smallest square containing the query
    Encode ranges into ternary vector
    If query is in the range: HIT !
More space Short time
Less space Long time
Less space Short time
But require range-to-range encoding
query
query
query
Iteratively expand from query
Class green
Create squares from existing data
Using both methods

## Slide 9: Distance metric
L-infinity norm
  Realization of “Squares”
  Gray code varies 1b for neighbors
    Good for encoding ranges
    But has some restrictions
      Range Starts from
      length =
00
01
11
10
0*
1*
*1
*0
*0
Gray code
0
1
2
3
Query
Hit!
4-bit example
Gray code + offset ( postfix ) + Intersection
Offset
0
1
2
3
4
[3,5] = [2,5] [3:6]
5
Postfix grows with maximum range linearly !

## Slide 10: Distance metric
L-1 norm ( Hamming distance)
  Finds the difference of bit data
V
Low Vt Sence Amp
High Vt Sence Amp
B
A
AB = 00 / 10 / 11
Diff = 2 1 0
Can binary bits represent integer L-1 norm well?
1 0 1 1 0 0 1 1
1 1 0 0 0 0 1 1
1
2
0
0
+
3
15-11=4 but 1111–1011 = 1
Thermometer code
0 -> 00000000
3 -> 00000111
5 -> 00011111
Avoids using ADC

## Slide 11: Problems of Best-Match TCAM
Analog non-idealities
  Noise of storage elements accumulates
  Parasitic effects of Match-Line
noise
noise
noise
noise
Large variation

## Slide 12: Problems of Best-Match TCAM
Analog non-idealities
  Noise of storage elements accumulates
  Parasitic effects of Match-Line
Position affects discharge rate
Mismatch here are less sensitive
( large denominator )
Mismatch here are more sensitive
( small denominator)
Match : small G
Mismatch : large G
RAM array
Eq. ckt model
To ADC
ML
To ADC

## Slide 13: Problems of Best-Match TCAM
Analog non-idealities
  Noise-aware training (CIM case)
    Noise of analog circuits could hazard our performance
    Inject noise into model to make it noise-resistant
or more complicated
device noise model (costly)
w/o noise injection
w/ noise
injection
What if we inject noise into embeddings?