## Slide 1: Design Technology Co-Optimization for In-Memory Search
Speaker: B11901027 王仁軒

## Slide 2: Outline
Introduction to few-shot learning
Traditional computer architecture vs In-memory searching
Choices of memory
  Volatile vs Non-volatile
Searching methods
  Exact-Match vs Best-Match
Distance metrics and its realization
  L-infinity norm
  L-1 norm
Difficulties of Best-Match searching method
  Methods to tackle analog non-idealities

## Slide 3: Few/One Shot Learning
Traditional classification models suffers from catastrophic forgetting when learning new domains
Tackle the forgetting issue
  Search ALL data stored in the memory
Classfier
Forgets about cats
  Cosine similarity!

## Slide 4: Traditional computer architecture
Traditional computer requires frequent data transfer between CPU and RAM for ML tasks
In memory search structure
  60%↑power
  von Neumann bottleneck
  Parallel !
  Scalable !
  0
  0
  0
  1
The array structure of memory allows us to lower the complexity of computing

## Slide 5: Types of Memory
Volatile vs Non-Volatile
16T CMOS
Cannot cut off power
LEAKAGE!!!
2T Flash/FeFET
Low power
Low leakage
2T RRAM Crossbar
Low power
Acceptable leakage

## Slide 6: Types of Searching
Exact-match vs Best-match TCAM
0
1
0
1
1
0
2
0
HIT !
HIT !
Difference
Don’t require complex circuit for post processing | Require other analog circuit (Winner Take All ckt, ADC…)
Can scale up to MB/GB | Scale is limited to kB due to analog non-idealities and area
Functionality is restricted (need Special Encoding) | Finds the most similar entry (hamming distance)

## Slide 7: Distance metric
Cosine similarity
Not friendly for direct hardware implementation
Need some distance metric that can be easily computed with binary data

## Slide 8: Distance metric
L-infinity norm
  Find the smallest square containing the query
    Encode ranges into ternary vector
    If query is in the range: HIT !
00
01
11
10
0*
1*
*1
*0
*0
Gray code
Good for encoding ranges
More space
Short time
Less space
Long time
Less space Short time
But require range-to-range encoding
query
query
query
000
001
011
010
110
111
101
100
Query
Hit!

## Slide 9: Distance metric
L-1 norm ( Hamming distance)
  Finds the difference of bit data
V
Low Vt Sence Amp
High Vt Sence Amp
B
A
AB = 00 / 10 / 11
Diff = 0 1 2
Can binary bits represent integer L-1 norm well?
1 0 1 1 0 0 1 1
1 1 0 0 0 0 1 1
1
2
0
0
+
3
15-11=4 but 1111–1011 = 1
Thermometer code
0 -> 00000000
3 -> 00000111
5 -> 00011111

## Slide 10: Problems of Best-Match TCAM
Analog non-idealities
  Noise-aware training
    Noise of analog circuits could hazard our performance
    Inject noise into model to make it noise-resistant
w/o noise injection
w/ noise
injection
or more complicated
device noise model (costly)
Noisy!