## Slide 1: Title
Speaker : B11901027 王仁軒
Mentor : Rick Huang
Advisor: Prof. An-Yeu (Andy) Wu
Date : 2025/05/02

## Slide 2: Outline

## Slide 3: Analog Non-Ideal Effects of TCAM
TCAM : Ternary content addressable memory
Analog non-ideal effects of in-memory-search
Noise from memory device
Thermal noise
Flicker noise
Leakage current
Parasitic effects of lump elements
Resistance
Capacitance

## Slide 4: Method 1 : Noise-Aware Training
Noise-Aware Training
  Inject simulated noise into embeddings while training the model
  Evaluate the Trained model on different noise levels
Embedding
Model
Training
+
+
+
+
Model
Noisy Embedding
Testing
Train on cloud server
Simulate noisy device by injecting noise to embeddings
Deploy the model to device
Simulate the device on server

## Slide 5: Method 2 : Bayesian Neural Network
Bayesian Neural Network (BNN)
  Train a robust model that embraces noise
  BNN minimizes KL-divergence (maximize Evidence Lower Bound, ELBO)
CNN
BNN
Loss : Cross Entropy
Loss : KL-divergence
Mean of cross entropy loss acorss samples
Ensure robustness against noise

## Slide 6: Robustness Against Noise
Both method works well on different datasets
  Trade-off between accuracy on clean data & noise tolerance
Tolerance against large noise
  Little noise has great effect
Chart: Noise-Aware Training (MNIST)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Baseline | 94.37 | 93.51 | 92.54 | 91.3 | 89.92 | 88.44 | 86.86 | 85.09 | 83.26 | 81.42 | 79.57
Noise Aware | 89.04 | 89.18 | 89.09 | 89.17 | 89.16 | 89.14 | 89.09 | 89.1 | 89.09 | 89.11 | 89.13
Bayesian NN | 90.7 | 90.92 | 91.02 | 90.97 | 90.99 | 90.98 | 90.93 | 90.88 | 90.83 | 90.79 | 90.76
Chart: Noise-Aware Training (Omniglot)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
Baseline | 89.24 | 87.55 | 85.72 | 84.05 | 82.36 | 80.75 | 79.23 | 77.69 | 76.16 | 74.69 | 73.32
Noise Aware | 86.74 | 86.69 | 86.76 | 86.75 | 86.72 | 86.69 | 86.69 | 86.69 | 86.7 | 86.73 | 86.72
Bayesian NN | 84.29 | 84.3 | 84.22 | 84.23 | 84.23 | 84.21 | 84.16 | 84.06 | 84.07 | 84.03 | 84.04
Chart: Effect of Different Noise STDEV
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
σ 0.00 | 82.78 | 79.92 | 76.6 | 73.49 | 70.65 | 68.11 | 65.88 | 63.91 | 62.1 | 60.5 | 59.05
σ 0.02 | 81.69 | 81.33 | 80.9 | 80.25 | 79.49 | 78.75 | 77.98 | 77.24 | 76.52 | 75.83 | 75.13
σ 0.10 | 78.63 | 78.82 | 78.85 | 78.82 | 78.81 | 78.71 | 78.61 | 78.52 | 78.43 | 78.27 | 78.15
High acc.
large noise

## Slide 7: 2-D Data Visualization
Visualize data using t-SNE
  Visualization method that maintains spatial distance
  Map angular distance to spatial distance using Locality-Sensitive Hashing
1
0
Closer data has similar hashed result
Random
hash vectors
1
0
1
0
0
0
Unwanted behavior due to cosine distance

## Slide 8: 2-D Data Visualization with LSH
Visualization Result
Baseline
Noise-Aware Training
Bayesian NN
Large Noise
Zero Noise
Low accuracy

## Slide 9: Origin of Noise Resilience in NN
Collect the value of every embeddings
  Blue : Original embedding value distribution
  Orange : New distribution on simulated noisy device
27 % accuracy
Noise dominates the embedding
Baseline
Noise-Aware Training
92 % accuracy
Noise has little impact on embedding
88 % accuracy
Noise has almost no impact on embedding
Bayesian NN

## Slide 11: From Angular to Distance Metric
Cosine similarity
Compute floating-point value is costly
Quantize the model to int
Computation cost
Use other metric rather than cos_sim
Hamming Distance ?
norm : d1 + d2 ?
norm : Max( d1 , d2 ) ?
Norm : d
d1
d2
Int8 for each dimension

## Slide 12: Exact-Match Search with Norm
norm – Using exact-match search
  Find the smallest square containing the query
  Encode ranges into ternary vector
    Represent a square using ranges
    If query is in the range: HIT !
More space Short time
Iterative !
Less space Long time
query
query
Iteratively expand from query
Class green
Create squares from existing data
1
2
3
1
Ref: Encoding Short Ranges in TCAM Without Expansion: Efficient Algorithm and Applications

## Slide 13: Range Encoding
norm
  Realization of “Squares”
  Gray code varies 1b for neighbors
    Good for encoding ranges
    But has some restrictions
      Range Starts from
      length =
00
01
11
10
0*
1*
*1
*0
*0
Gray code
0
1
2
3
4-bit example
Gray code + offset ( postfix ) + Intersection
Offset
0
1
2
3
4
[3,5] = [2,5] [3:6]
5
Ref: Encoding Short Ranges in TCAM Without Expansion: Efficient Algorithm and Applications
Range = 2 OK
Range = 3 Fail
**

## Slide 14: Best-Match Search with Norm
norm ( Hamming distance) – Using best-match search
  Regular method : Use 8-bit ADC
  Method to avoid using ADC : cut the data into segments
V
Low Vt Sence Amp
High Vt Sence Amp
B
A
AB = 00 / 10 / 11
Diff = 2 1 0
Can binary bits represent decimal norm well?
1 0 1 1 0 0 1 1
1 1 0 0 0 0 1 1
1
2
0
0
+
3
15-11=4 but 1111–1011 = 1
Thermometer code
0 -> 00000000
3 -> 00000111
5 -> 00011111
Avoids using 2-bit ADC
Ref: SAPIENS: A 64-Kbit RRAM-Based Non-Volatile Associative Memory for One-Shot Learning and Inference at the Edge

## Slide 15: Problems of Best-Match TCAM
Analog non-idealities
  Noise of storage elements accumulates
  Parasitic effects of Match-Line
noise
noise
noise
noise
Large variation
Ref: Experimentally validated memristive memory augmented neural network with efficient hashing and similarity search

## Slide 16: Problems of Best-Match TCAM
Analog non-idealities
  Noise of storage elements accumulates
  Parasitic effects of Match-Line
Position affects discharge rate
Mismatch here are less sensitive
( large denominator )
Mismatch here are more sensitive
( small denominator)
Match : small G
Mismatch : large G
RAM array
Eq. ckt model
To ADC
ML
To ADC
Ref: In-Memory Nearest Neighbor Search With Nanoelectromechanical Ternary Content-Addressable Memory

## Slide 17: Overcome Analog Non-Ideal Effects
Analog non-idealities
  Noise-aware training (Compute-in-memory case)
    Noise of analog circuits could hazard our performance
    Inject noise into model to make it noise-resistant
or more complicated
device noise model (costly)
w/o noise injection
w/ noise
injection
What if we inject noise into embeddings?
Ref: In-Memory Computing Advances and Prospects

## Slide 18: Conclusions and Future Work
Choices of memory
  Non-volatile memory can be compact and energy-efficient
Searching methods
  Use exact-match for big tasks and best-match for small tasks
Distance metrics
  Use and Norm to replace cosine similarity
Challenges of best-match search
  Analog noise and parasitic effects are challenging
Future Work
  Apply the method used in CIM to Overcome Analog non-ideal effects
  Does and Norm performs as good as cosine similarity